## Slide 1: Optimization Techniques in ARMv7 Assembly Programming: Fibonacci Sequence
By Rojan Shrestha
CSE2312

## Slide 2: Brief overview of ARMv7 architecture
A low-level programming language that provides direct control over hardware.
ARMv7 is a 32-bit RISC architecture commonly used in mobile and embedded systems.
Uses mnemonic codes and labels to represent machine-level instructions

## Slide 3: Characteristics
Hardware-Specific: Tied closely to a computer's architecture (e.g., ARM, x86).
Efficiency: Allows for precise manipulation of hardware resources.
Readability: More readable than machine code but less abstract than high-level languages.

## Slide 4: Why optimization is crucial in assembly programming.
Optimization reduces execution time, saves energy, and maximizes the performance of hardware.
Optimization enables developers to produce faster, smaller, and more efficient programs, which is particularly important in resource-constrained or performance-critical environments.

## Slide 5: Fibonacci Sequence
What is the Fibonacci sequence?
A sequence where each number is the sum of the two preceding ones.
Recurrence relation: F(n) = F(n-1) + F(n-2).
Widely used in computer science to demonstrate recursion and iterative algorithms.
  Fibonacci sequence: 0 1 1 2 3 5 8 13 21 34 55 89….

## Slide 6: Unoptimized ARMv7 Assembly Code
Iteratively calculates each Fibonacci number.
Stores results in memory after each computation.
fibonacci:
MOV R0, #0
MOV R1, #1
LDR R2, =fibonacci_sequence
STR R0, [R2], #4
STR R1, [R2], #4
MOV R3, #2 ; Loop counter starts at 2
LDR R4, [sp] ; Desired sequence length
loop:
CMP R3, R4
BGE end
LDR R0, [R2, #-8] ; Load Fib(n-2)
LDR R1, [R2, #-4] ; Load Fib(n-1)
ADD R0, R0, R1 ; Calculate Fib(n)
STR R0, [R2], #4 ; Store Fib(n)
ADD R3, R3, #1 ; Increment counter
B loop
end:
BX LR

## Slide 7: Limitations of the Unoptimized Code
Excessive memory access.
LDR R0, [R2, #-8], LDR R1, [R2, #-4] and STR R0, [R2], #4 access memory in each iteration
Inefficient use of CPU cycles.
    Poor utilization of available CPU instructions leads to longer execution times.
Limited use of ARM's advanced features.
    Unoptimized code does not take advantage of ARM's pipelining and register capabilities.
    Potential for Pipeline Stalls.
Dependent instructions may cause delays if the previous instruction's result isn't ready.
For example, using R0 immediately after it's calculated.

## Slide 8: Optimization Techniques Applied
Loop Unrolling: Reducing the number of loop iterations by expanding the loop body.
Memory Access Management: Minimizing memory access by using registers effectively.
Instruction Pipelining: Rearranging instructions to reduce pipeline stalls.

## Slide 9: Loop Unrolling
What is Loop Unrolling?
Technique to reduce loop control overhead by expanding the loop body.
Unrolled Loop:
Executes multiple iterations within a single loop iteration, reducing branching.
Code Changes:
Expanded the loop to calculate two Fibonacci numbers per iteration.

## Slide 10: Loop Unrolling
fibonacci:
MOV R0, #0
MOV R1, #1
LDR R2, =fibonacci_sequence
STR R0, [R2], #4
STR R1, [R2], #4
MOV R3, #2
LDR R4, [sp]
loop:
CMP R3, R4
BGE end_loop
LDR R0, [R2, #-8]
LDR R1, [R2, #-4]
ADD R5, R0, R1
STR R5, [R2], #4
ADD R3, R3, #1
CMP R3, R4
BGE end_loop
LDR R0, [R2, #-8]
LDR R1, [R2, #-4]
ADD R5, R0, R1
STR R5, [R2], #4
ADD R3, R3, #1
B loop
end_loop:
BX LR

## Slide 11: Performance Impact of Loop Unrolling
Reduced Loop Control Overhead
  Fewer branch instructions, which reduces CPU cycles spent on loop control.
  Impact: Overall improvement in execution time due to reduced loop iterations.
Performance Metrics:
  Execution Time: Reduced compared to the unoptimized version.
  CPU Cycles: Decreased due to fewer branching operations.

## Slide 12: Memory Access Management Optimization
Instead of frequently accessing memory, use registers to store intermediate values.
Reduced memory load/store operations by keeping Fibonacci values in registers.
Reduced memory latency by minimizing load/store instructions.
ADD R5, R0, R1
STR R5, [R2], #4
MOV R0, R1
MOV R1, R5
ADD R3, R3, #1

## Slide 13: Benefits of Memory Access Optimization
Lower Memory Latency
  Fewer memory accesses lead to reduced wait times for data retrieval.
  Impact: Improved execution speed due to faster data access.
Performance Metrics:
  Execution Time: Significantly improved compared to unoptimized code.
  CPU Cycles: Reduced as fewer memory operations are needed.

## Slide 14: Instruction Pipelining Optimization
What is Instruction Pipelining?
  Reorganizing instructions to ensure that the CPU pipeline remains filled, reducing stalls.
Optimized Code:
  Rearranged instructions to minimize dependencies between consecutive operations.

## Slide 15: Instruction Pipelining Optimization
fibonacci:
MOV R0, #0
MOV R1, #1
LDR R2, =fibonacci_sequence
STR R0, [R2], #4
STR R1, [R2], #4
MOV R3, #2
LDR R4, [sp]
loop_pipeline:
CMP R3, R4
BGE end_loop
ADD R5, R0, R1 // Calculate next Fibonacci value
STR R5, [R2], #4 // Store the result in memory
ADD R3, R3, #1 // Increment the loop counter
MOV R0, R1 // Update R0 to the previous R1
MOV R1, R5 // Update R1 to the new Fibonacci value
B loop_pipeline
end_loop:
BX LR

## Slide 16: Pipelining Impact
Reduced Pipeline Stalls
  By reordering instructions, dependencies are minimized, allowing the CPU to execute instructions without stalling.
  Impact: Increased instruction throughput and improved performance.
Performance Metrics:
  Execution Time: Further reduced due to minimized stalls.
  CPU Utilization: Improved as the pipeline is kept busy.

## Slide 17: Performance Gains Summary
Loop Unrolling: Reduced loop control overhead.
Memory Access Management: Minimized memory latency by using registers.
Instruction Pipelining: Increased CPU efficiency by reducing stalls.

## Slide 18: Real-World Applications
Where are These Techniques Used?
  Embedded Systems: Optimized assembly code is crucial in resource-constrained environments.
  Video Game Engines: Performance-critical parts are often optimized using assembly to achieve higher frame rates.
  Signal Processing: Assembly optimizations help in minimizing latency and maximizing throughput.
Impact: Highlight how these optimizations are essential in making systems more efficient and responsive.

## Slide 19: Potential Further Optimizations
SIMD Instructions: Explore using SIMD for parallel computations to further enhance performance.
Cache Optimization: Investigate techniques for making better use of the CPU cache to further reduce memory latency.
Advanced Pipelining Techniques: Explore other forms of instruction-level parallelism for further gains.
Branch Prediction Optimization: Implement branch prediction techniques to reduce delays due to branch mispredictions.
Increased Register Usage: Allocate more variables to registers instead of memory, effectively reducing memory bottlenecks further.
Loop Fusion: Combine multiple loops into a single loop to minimize overhead, if applicable.

## Slide 20: Questions?

## Slide 21: Thank you all for your time and attention